GABONA-LABOR Ltd.		Calibration Laboratory

Reference number:  89/2005.

Number of calibration:13/2005

Date: 26. 09. 2005.

Registration number of the accreditation: 2-0197:2003 by NAT.

# REFERENCE MATERIAL CERTIFICATE

1 /2 page

1. Name of the RM: 		Set of WHEAT (grain).

2. Destination of the RM: 	- control of measures,

- calibration of different kind of measuring equipment, 					- validation of measurements

3. Method of the certification:	The certified and indicative values were stated by 	evaluating the measuring results of the accredited laboratory of Hungary according 	to the ISO IEC GUIDE 35:1989 (Certification of reference materials - General and 	statistical principles)

4. Certified values and its uncertainty:

| Certified values | Wheat |
| --- | --- |
|  | 1. Sample | 2. Sample | 3. Sample |
| Protein % (m/m) (Nx5,7) dry matter | 14,84 0,10* | 12,17 0,10 | 12,08 0,10 |
| Wet glutein % (m/m) | 34,7 0,5 | 26,9 0,3 | 25,8 0,3 |
| Ash %(m/m) dry matter | 1,86 0,02 | 1,75 0,02 | 1,71 0,02 |
| Falling number S (grinded wheat) | 494 11 | 365 8 | 294 8 |
| Falling number S (Laboratory flour) | 501 15 | 367 9 | 326 8 |
| Water absorption % (m/m) | 66,4 0,5 | 56,3 0,4 | 59,4 0,4 |
| Sedimentation index (Zeleny test) ml | 40,5 3,0 | 30,4 1,4 | 39,1 1,8 |

2/2 page

Indicative values:

| Moisture content % (m/m) | 1. Sample | 2. Sample | 3. Sample |
| --- | --- | --- | --- |
|  | 10,8 0,1 | 11,0 0,1 | 10,8 0,1 |

*The reported expanded uncertainty of measurement is stated as the standard uncertainty of measurement multiplied by the coverage factor k=2, which for a normal distribution corresponds to a coverage probability of approximately 95 %. The standard uncertainty of measurement has been determined in accordance with EAL Publication EAL-R2.

5. Packing:  moisture proof foil.

After opening the foil the sample should be stored in an air-tight vessel

6. Storage temperature:  15 – 30 ºC.

7. Mass of the material:  3 x 700 g

8. The date of the certification:  10. May 2005.

9. The certified value is valid:  to 31 December 2005.

Number of calibration mark: 89/13/2005.

The certification was controlled and authorized by:

dr. Judit BUDAI

Head of the Laboratory

Senior officer of metrology

Copy of this certificate is alowed only in full.

Calibration Laboratory					( / fax:	       36/1/2200 359

( 1144. Budapest,							( / fax:	    36/1/22 33 384

Vezér u. 59/d.  fsz.1.	    e-mail: gabonalabor@chello.hu	(:	          36/06/20 324-9221

The Head Office: ( 1141. Budapest, Tihany tér 7. HUNGARY  (/fax: 	         36/1/ 2200-359