GABONA-LABOR Ltd.		Calibration Laboratory

Reference number:  /2006.

Number of calibration: /2006.

Date: 24. 02. 2006.

Registration number of the accreditation: 2-0197:2003 by NAT.

# REFERENCE MATERIAL CERTIFICATE

1 /2 page

1. Name of the RM: 		Set of WHEAT -FLOUR

2. Destination of the RM: 	- control of measures,

- calibration of different kind of measuring equpment, 					- validation of measurements

3. Method of the certification:	The certified and indicative values were stated by 	evaluating the measuring results of the accredited laboratory of Hungary according 	to the ISO IEC GUIDE 35:1989 (Certification of reference materials - General and 	statistical principles)

4. Certified values and its uncertainty:

| Certified values | Wheat- Flour |
| --- | --- |
|  | 1. Sample | 2. Sample | 3. Sample |
| Protein % (m/m) (Nx5,7) dry matter | 14,06 0,10 | 13,76 0,10 | 10,95 0,10 |
| Wet glutein % (m/m) | 30,4 0,4 | 29,7 0,3 | 25,8 0,3 |
| Ash %(m/m) dry matter | 0,49 0,01 | 0,87 0,01 | 0,60 0,01 |
| Falling number s | 352 9 | 335 5 | 354 6 |
| Walue of W Rheological p properties G | 231,9 20,8 89,3 8,5 20,4 1,1 | 251,6 30,4 114,6 11,2 17,9 1,4 | 200,2 29,7 113,6 27,5 17,3 1,3 |
| Water absorption* % (m/m) | 60,5 0,8 | 64,8 1,1 | 61,4 1,3 |
| Backing quality det.* | 76,3 4,6 | 77,1 2,6 | 70,0 2,5 |
| Dough Stability time* | 2,5 0,8 | 2,0 0,3 | 2,3 0,4 |
| Degree of Softening* | 44,7 7,3 | 51,5 8,4 | 56,8 10,4 |

2/2 page

Indicative values:

| Moisture content % (m/m) | 1. Sample | 2. Sampl | 3. Sampl |
| --- | --- | --- | --- |
|  | 14,06 0,1 | 13,47 0,1 | 13,81 0,1 |

- Determination by Faringraph.

The reported expanded uncertainty of measurement is stated as the standard uncertainty of measurement multiplied by the coverage factor k=2, which for a normal distribution corresponds to a coverage probability of approximately 95 %. The standard uncertainty of measurement has been determined in accordance with EAL Publication EAL-R2.

5. Packing:  moisture proof foil.

After opening the foil the sample should be stored in an air-tight vessel.

6. Storage temperature: 	15 – 30 ºC.

7. Mass of the material: 	3 x 500 g

8. The date of the certification: 	20. Dec. 2005.

9. The certified value is valid: 	to 31. Junius 2006.

Number of calibration mark: 0/0/2006.

The certification was controlled and authorized by:

dr. Judit BUDAI

Head of the Laboratory

Senior officer of metrology

Copy of this certificate is alowed only in full.

Calibration Laboratory					( / fax:	        36/1/2200 359

( 1144. Budapest,							(		     36/1/22 33 384

Vezér u. 59/d.  fsz.1.  e-mail: gabonalabor@chello.hu		(:	       36   /06/20 324-9221

The head Office: ( 1141. Budapest, Tihany tér 7. HUNGARY	(/fax:        36/1/ 2200-359